## Slide 1: Physics Unit 5 - Electricity
Notes: 1
1

## Slide 2: Electric Charges
In chemistry: matter is made up of atoms which are made of protons, electrons, and neutrons
Electric charges of these particles:
  Protons – positive
  Electrons – negative
  Neutrons – neutral
  (no charge)

## Slide 3: Electric Charges
Force is exerted between any two things that have an electric charge
  opposite charges attract
  like charges repel

## Slide 4: Conductors
Conductor – material that allows electrons to move through it easily
  e- (electrons) are loosely held
  ex: metals like copper and silver

## Slide 5: Insulators
Insulator – material that doesn’t allow electrons to move through it easily
  e- are tightly held
  ex: plastic, wood, rubber, glass

## Slide 6: Static Electricity
Static Electricity – the net accumulation of electric charges on an object
Charging – electric charges are transferred from one object to another, total charge is conserved

## Slide 7: Methods of Charging
Friction – the charging of an object by rubbing two items together
Charges separate (one object becomes more negative, the other more positive)
EX:

## Slide 8: Methods of Charging
Induction – rearrangement of particles to produce a positive side and negative side
Charges move within an object, not between objects
EX:

## Slide 9: Methods of Charging
Conduction – transfer of charge from one object to another by direct contact
Charges even out between objects
EX:
electroscope

## Slide 10: Static Discharge
The movement of electrons to relieve a separation in charge
  EX: sparks, lightning

## Slide 11: Electrical Quantities
Potential Difference
Current
Resistance

## Slide 12: Potential Difference
Potential Difference/Voltage (V) – difference in electrical potential between two places
  large separation of charge creates high voltage
  the “push” that causes e- to move from - to +
  measured in volts (V)

## Slide 13: Batteries
Wet cell – uses a liquid (wet) electrolyte.
  Ex: car battery
Dry cell – uses a non-liquid (dry) electrolyte.
  Ex: flashlight battery, AA, AAA, C, D
Battery – device that converts chemical energy into electrical energy
  Provides a consistent voltage (Ex: 9V)
  Uses an electrolyte that allows charges to move from one electrode to another

## Slide 14: Current
Current (I) – flow of electrons through a conductor
  depends on # of e- passing a point in a given time
  measured in amperes (A)

## Slide 15: Resistance
Resistance (R) – opposition to the flow of electrons
  Converts electrical energy to thermal energy & light
  measured in ohms ()
Copper - low resistance
Tungsten - high resistance

## Slide 16: Resistance Depends on:
Resistivity/type of material
  Conductors have low resistivity, insulators have high resistivity
Thickness of wire
  Increasing thickness decreases resistance (easier to drink from a wide straw)
Length of wire
  Increasing length increases resistance (harder to drink from a long straw)
Temperature
  Increasing temperature increases resistance

## Slide 17: Ohm’s Law
Ohm’s Law
V = I × R
V: potential
difference (V)
I: current (A)
R: resistance ()

## Slide 18: Ohm’s Law
Ohm’s law: V=IR is like Newton’s 2nd Law: F=ma
Current increases when voltage increases.
  Stronger push in the circuit, more flow.
  Like stronger force = larger acceleration
Current decreases when resistance increases
  More resistance to flow, less flow
  Like larger mass = smaller acceleration

## Slide 19: Ohm’s Law
A lightbulb with a resistance of 160  is plugged into a 120-V outlet. What is the current flowing through the bulb?
GIVEN:
R = 160 
V = 120 V
I = ?
WORK:
I = V ÷ R
I = (120 V) ÷ (160 )
I = 0.75 A
I
V
R

## Slide 20: Electrical Power
Electrical Power
  rate at which electrical energy is converted to another form of energy
P = I × V
P: power (W)
I: current (A)
V: potential
difference (V)

## Slide 21: Electrical Power
Electric companies charge for use of electricity based off of amount of energy used
  Remember P=W/t so W=P x t
  The amount of electrical energy used is electrical power x time
  Units: kilowatt-hour (1000 W x 3600 s)

## Slide 22: Electrical Power
A calculator has a 0.01-A current flowing through it. It operates with a potential difference of 9 V. How much power does it use?
GIVEN:
I = 0.01 A
V = 9 V
P = ?
WORK:
P = I · V
P = (0.01 A) (9 V)
P = 0.09 W
I
P
V

## Slide 23: Circuits
Circuit – closed path through which electrons can flow

## Slide 24: Circuit Components – Symbols
Battery
Resistor
Wire
Junction
Light bulb
Switch

## Slide 25: Circuit Components - Diagram
A - battery C - light bulb E - wire
B - switch D - resistor F - junction
E
F

## Slide 26: Series Circuits
Objects are arranged one after another.
Current only has one path to travel.
Current is the same through all objects.

## Slide 27: Series Circuits
  current travels in a single path
    one break stops the flow of current
  current is the same throughout circuit
    lights are equal brightness
  each device receives a fraction of the total voltage
    get dimmer as lights are added

## Slide 28: Parallel Circuits
Objects are arranged one beside another.
Current has more than one path to travel.
Current is split up between paths.

## Slide 29: Parallel Circuits
  current travels in multiple paths
    one break doesn’t stop flow
  current varies in different branches
    takes path of least resistance
    “bigger” light would be dimmer
  each device receives the total voltage
    no change when lights are added

## Slide 30: Household Circuits
Combination of parallel circuits
  too many devices can cause wires to overheat
Safety Features:
  fuse - metal melts, breaking circuit
  circuit breaker - bimetallic strip bends when hot, breaking circuit